## Slide 1
SENTINEL
Unified CCTV Intelligence Platform
One operational picture across every departmental camera in Gujarat — without moving the video.
Gujarat Police Innovation Challenge 2026 · Model 1 + Model 3
Notes: SENTINEL addresses Model 1, the compulsory statewide camera registry with GIS mapping, and Model 3, a middleware federation layer. Departments keep their own cameras, storage and retention policy.

## Slide 2
THE PROBLEM
Every department already has cameras. Nobody has the picture.
Police, municipal, transport and health estates each run their own DVRs, NVRs and vendor VMS. The footage exists. Reaching it is a phone call, a trip, and a USB stick.
1
Islands of evidence
Each estate is a separate system with its own login, format and retention. No query crosses them.
2
Investigation by legwork
Tracing one vehicle means contacting each department in turn and hoping the clip still exists.
3
Rip-and-replace is not an option
Departments will not surrender control of their cameras, their storage, or their budgets.

## Slide 3
THE DESIGN DECISION EVERYTHING FOLLOWS FROM
Move metadata, not video.
Analytics runs at the edge or on a regional node. Only compact structured records travel to the centre. Video moves when, and only when, there is a hit worth looking at.
Centralising the streams
160
Gbps sustained backhaul
52 PB
at 30-day retention
80,000 cameras at 2 Mbps each.
Centralising the metadata
16 GB
per day, whole state
~10,000x
less network load
The same grid, carrying plate reads instead of pixels.
Figures are order-of-magnitude estimates for a statewide estate at the stated assumptions.

## Slide 4
ARCHITECTURE
Three tiers, one event interface
The same codebase runs as a district edge node or as the central server. Configuration decides which.
Departmental systems
DVR, NVR and vendor VMS stay exactly where they are. No replacement, no migration, no change of ownership.
→
Edge / regional node
Adapter, decode, detect, ANPR and face matching. A durable SQLite spool holds results when the link drops.
→
Central tier
Registry, metadata index, watchlist matching, alerting and the GIS console for the whole state.
Metadata only travels right. Video is pulled left, on demand, only against a hit.

## Slide 5
MODEL 1 · THE COMPULSORY FOUNDATION
Statewide camera registry with GIS
Every camera carries its position, orientation and reach, so coverage is a map question rather than a spreadsheet question.
Geospatial record
Latitude, longitude, compass heading, field of view and nominal ground range for each camera.
Live health
Online, offline or unknown, with last-seen timestamps and per-department rollups.
Coverage and gaps
The map shows which junctions are watched and, more usefully, which are not.
Vehicle localisation
Detections carry a normalised ground-contact point, so a sighting projects onto real coordinates.

## Slide 6
MODEL 3 · FEDERATION MIDDLEWARE
Four adapters, one normalised event
Each adapter speaks one departmental system and returns the same shape. Adding a vendor is a new adapter, not a new platform.
Sentinel grid
RTSP, HLS and WebRTC-WHEP against the state feed, with credentials redacted in every log and export.
ONVIF Profile S
WS-Discovery scan of a local network, then probe and onboard. Off by default: multicast is nobody's surprise.
Manual RTSP
Any RTSP device or DVR channel, configured by name and URL. The fallback that always works.
Local media archive
A directory of recorded files federated as a second, non-network system for replay and testing.
RTSP is forced over TCP throughout; timing is driven by stream presentation timestamps, not arrival time.

## Slide 7
NUMBER PLATE RECOGNITION
A vehicle-first cascade, not a full-frame sweep
Tiled full-frame plate detection measured 4 to 8 seconds per frame and produced unusable reads. Finding the vehicle first is faster and recalls more.
1
Detect vehicles
YOLO at 960px isolates cars, motorcycles, buses and trucks in the full frame.
2
Find the plate
A dedicated plate detector runs on each upscaled vehicle crop, gated on aspect ratio and minimum width.
3
Read the characters
An Indian-tuned PP-OCRv5 recogniser, exported to ONNX, reads the plate region.
4
Agree on an answer
Reads are grouped into tracks and confirmed once two agree within an edit distance of two.
Single-frame reads of one physical plate disagree. Consensus is what makes the output usable as evidence rather than as a suggestion.

## Slide 8
THROUGHPUT
The same pipeline, on the GPU
One configuration setting moves every model onto CUDA. It is verified by executing a graph on the device, because the runtime advertises the provider whether or not it works.
Chart: Median milliseconds per frame, 1080p
| CPU | CUDA
Median milliseconds per frame | 1186 | 523
2.3x
faster end to end
1.91
frames per second
718 MB
peak VRAM of 4 GB
Measured on an NVIDIA GTX 1650 against live grid frames.

## Slide 9
WATCHLISTS
Vehicles are half the problem statement
The brief names wanted persons and missing persons. A plate reader cannot answer either, so face recognition runs alongside it.
Vehicle watchlist
Stolen, wanted, suspect or expired. Matching is fuzzy, so a misread plate still raises the alert.
Person watchlist
A wanted or missing person is enrolled from one photograph; the grid arms itself against that face.
Zero cost when idle
The face pass only runs when somebody is actually enrolled, and is capped so it cannot saturate the node.
Live alerting
Matches broadcast over a websocket to every open console, with the snapshot that triggered them.

## Slide 10
THE TEST CASE
Plate number in, movement history out
One query returns the route, the validation summary, the registration record and the watchlist verdict, so an investigator never has to know which system holds what.
What comes back
Timestamped, location-wise sighting chain
Reconstructed path drawn on the GIS map
Owner and registration from the vehicle authority
Watchlist status and any open alerts
Court-ready CSV and PDF export
Spatio-temporal validation
Consecutive sightings are checked against the distance between the two cameras and the time elapsed. A hop nobody could have driven is flagged in the route rather than quietly presented as fact.
This is what separates a plate search from an evidence trail: the system states when it does not believe itself.

## Slide 11
EVIDENCE
Artifacts an investigating officer can file
The export is built to be handed to a court, not to be screenshotted into a report.
Movement report, PDF
Registration block, embedded snapshot thumbnails, chronological sighting log and officer signature blocks.
Hashed snapshots
A SHA-256 digest is recorded against every captured image and printed beside each record.
Chain of custody
A written statement of how the records were produced, and an explicit note that nothing was reordered or filtered.
Reproducible
The document regenerates identically from the same database state and stated timestamp.

## Slide 12
GOVERNMENT SYSTEMS
One subject, every authority's view
A query fans out across every connector with a view of the subject, so the officer gets one answer per authority instead of having to know which database holds the answer.
VAHAN
Vehicle registration, owner, make, model and fuel class
eGujCop
State police records, including stolen-vehicle reports
CCTNS
Crime and criminal tracking network records
AFIS / NAFIS
Biometric identification for person subjects
One authority failing must not lose the others. Each connector answers or reports itself unavailable, and the investigator sees which did which.
Connectors run against documented record shapes; live endpoints are supplied at deployment.

## Slide 13
ACCOUNTABILITY
A surveillance system is bought on its controls
Capability is the easy half. What a department is procuring is the answer to who did what, under what authority, and whether it can be proved afterwards.
Three roles, one gate
Viewer, operator and administrator. Enforcement lives in a single middleware, so a new endpoint is closed by default rather than open.
Accounts a control room can run
Multiple operators per shift, created and revoked by an administrator. Passwords are stored only as salted hashes.
Revocation that takes effect now
Deactivating an account, changing its role or resetting its password ends every session it holds on the next request, not at token expiry.
Append-only audit trail
Every mutating call records the caller, the target and the outcome. Accounts are deactivated, never deleted, so the history stays attributable.

## Slide 14
ENGINEERING
Built and tested, not sketched
277
automated tests passing
72
API endpoints
15
console screens
13,400
lines of application code
4
federation adapters
8
persisted data models
Tests cover plate matching, role enforcement, account revocation, the edge spool, evidence export and the API end to end.

## Slide 15
NEXT
From working platform to system of record
The capability is there. The next phase is what turns it into something a department can operate and defend.
1
Case files
Investigations linked to an FIR number, with sightings, alerts and exports attached to the case rather than floating loose.
2
Purpose-bound search
Every trace records a case reference and a stated purpose, with a per-subject access log. Aligned to the Digital Personal Data Protection Act.
3
Jurisdiction scoping
Accounts scoped to a district or range, with cross-jurisdiction access requested explicitly and logged.
4
Operator review queue
Officers confirm or correct plate reads. Corrections become ground truth, and recognition accuracy becomes a measured, improving figure.

## Slide 16
Departments keep their cameras.
The state gets the picture.
SENTINEL · Unified CCTV Intelligence Platform · Gujarat Police Innovation Challenge 2026